## Slide 1: Ethical Mission Definition and Execution for Maritime Robotic Vehicles A Practical Approach
CRUSER TechCon
11 July 2016
Don Brutzman, Duane Davis, Curt Blais and Bob McGhee
Naval Postgraduate School (NPS), Monterey California USA

## Slide 2: Motivating challenge: ethics
How can robotic systems behave ethically?
  Important for military operations abroad
  Civil and scientific operations also coexist daily
Not necessarily about religion or morality
  Law of armed conflict internationally recognized
  Often captured as Rules of Engagement (ROE) guidance for teams of national or coalition forces
Legal basis under challenge: are robots unethical?
  Military readiness must be prepared for combat
  Opposing forces don’t read the same memos…

## Slide 3: Motivation: human-taskable maritime robots
We look to near-term future when UMVs can offload force projection, reduce danger to fleet
Variety of emerging robot solutions must remain compatible with human concepts and tasking
  Necessary for mission planning and justification
  Otherwise the robots are simply not autonomous
Extensive/exhaustive prelaunch testing is critical
  For mission confidence and in-water reliability
This work is building an extendable architecture…
  … for continued efforts bridging human, robot logic
Notes: Prelaunch testing includes both human and software rehearsal.

## Slide 4: Practical approach
Define missions that integrate ethical constraints without relying on artificial intelligence (AI) or obscure abstractions for appropriate behavior
  No embedded homunculus or abstract ethicist engine
Design robot missions in way that can be adapted to a variety of disparate robot paradigms
  Generally adaptable to tasking of diverse systems
Build on patterns that work well for human groups cooperating on difficult, dangerous tasks
  Human accountability remains central
  Otherwise still need human at end of remote tether

## Slide 5: Key insight #1
Humans in military units are able to deal with moral challenges without ethical quandaries
Careful definitions are provided for
  Tasks, missions, objectives, coordinated operations
  Ethical constraints and rules of engagement
These allow both measured and rapid response, independently and cooperatively
  Commanders do not deploy illegal, immoral weapons
  Unmanned systems must also pass similar scrutiny, otherwise commanders cannot utilize them

## Slide 6: Enabling factor: maritime environment
Major international controversy unfolding: drone use for conduct of reduced-risk warfare
  Many factors involved: technical, political, social
  Remote human “control” is highly questionable
  Complex, confounded environments
Maritime environment is much less ambiguous
  Fewer IFFN issues, identification friend foe neutral
  Presence of bad actors usually confirmable
  Law of Sea, Laws of Armed Conflict, etc.

## Slide 7: Goal-based Mission Example
Simple yet general mission goals, decision logic
Common approach, adaptable to other vehicles
Extendable and refinable mission tasking

## Slide 8: Example Goal-based Mission Definition
Goal 1. Proceed to Area A and search the area. If the search is successful execute Goal 2. If the search is unsuccessful, execute Goal 3.
Goal 2. Obtain environment sample from Area A. If the sample is obtained, execute Goal 3. If the sample cannot be obtained, proceed to recovery position to complete the mission.
Goal 3. Proceed to Area B and search the area. Upon search success or failure, execute Goal 4.
Goal 4. Proceed to Area C, rendezvous with UUV-2. Upon rendezvous success or failure, transit to recovery position to complete the mission.
Notes: Clumsy but readable. Humans can agree on intent.

## Slide 9: Goal-based Mission Example
Phase 1: Search Area A
Phase 2:
Sample Environment in Area A
Phase 3: Search Area B
Phase 4: Rendezvous with
UUV-2 in Area C
Succeed
Fail
Fail
Fail
Succeed
Succeed
MEA Start
Sample Environment Phase Controller
Area Definition
Sampling Requirements
Operational and Ethical Constraints Checking
Queries
Responses: Succeed
or Fail
Tactical Level
System State and Sensor Data
Controller Parameters
Sensor Settings, Responses
Phase 5: Transit
Return to Base
Succeed
Fail
Mission Abort
Mission Complete
Succeed
Fail
Execution Level
handles real-time control and response
Tactical-Level modules with shared vehicle state
and telemetry history
Vehicle
Commands
Strategic Level
Real-time orders
Tactics module sequencer
Surface
Recovery position
Robot mission conduct
can be independent of
software implementation
Notes: Right hand side: our robot architecture handles these task assignments one way. Another robot architecture may handle it a different way. Each however can be expected to sufficiently capable to report success or failure of each assignment. If not, then that robot is unresponsive and not really taskable with confidence by humans.

## Slide 10: Adding ethical constraints to mission requirements
Following the leader:
how do human teams accomplish tasks ethically?
The same rules need to apply to unmanned systems.

## Slide 11: Key insight #2
Ethical behaviors don’t define the mission plan.
rather
Ethical constraints inform the mission plan.

## Slide 12: Example ethical constraints: civil
Safe navigation, follow pertinent rules of road
Satisfactory navigational accuracy (GPS etc.)
Have received timely clearance to enter a specific geographic area for given time period
  Also vertical clearance for underwater depth zone or airborne altitude zone
Sufficient vehicle health, power, safety status
Meet communication requirements for tasking
  Identity beacon, transponder, AIS tracking, etc.
  Recording and reporting on situational data, etc.

## Slide 13: Civil ethical constraint support in AVCL, AUV Workbench
Civil ethical constraints | Define | Test | Notes
Mission tasking | √ | partial | AVCL goals
Safe navigation and transit | √ | √ | AVCL avoidance areas
Follow pertinent rules of road |  |  | Requires rule-engine path planner, sensing model
Satisfactory navigational accuracy (GPS etc.) | √ | √ | Needed: sensor error models
Clearance to enter a specific geographic area | √ | √ | 
Vertical clearance for underwater depth zone or airborne altitude zone | √ | √ | 
Timing requirements using specific times or duration | √ | √ | 
Sufficient vehicle health, power, safety status | partial | partial | 
Meet communication requirements for tasking | partial | partial | Message-passing scheme
Identity beacon, transponder, AIS tracking, etc. |  |  | 
Recording and reporting on situational data |  |  | 

## Slide 14: Example ethical constraints: military
Meet all relevant, international civil requirements
Identification friend foe (IFF), blue-force tracking
  friendly/hostile/neutral/unknown
Prior determination of contact’s hostile intent
  Robot option to warn without fear of self protection
ROE use of deadly force, weapons releasability
  Brevity codes: weapons safe, hold, tight, free
  Confirmation and permission requirements
After-action reporting, damage assessment
Et cetera, et cetera…

## Slide 15: Military ethical constraint support in AVCL, AUV Workbench
Military ethical constraints | Define | Test | Notes
Meet all relevant, international civil requirements | partial | partial | See above
Mission tasking | √ | partial | AVCL goals
Contact identification, tracking signatures |  |  | Available in C2 systems
Identification friend foe (IFF), blue-force tracking (friendly/hostile/neutral/unknown/etc.) |  |  | Available in C2 data models
Robot option to warn without fear of self protection |  |  | Implementable via messaging
Determination of contact’s hostile intent |  |  | Available in C2 data models, dissertation work in progress
Confirmation and permission requirements |  |  | Implementable via messaging
ROE use of deadly force, weapons releasability using brevity codes: weapons safe, hold, tight, free | partial | partial | Requires weapons model
Proportional weapons response |  |  | Requires weapons and threat models
After-action reporting | partial | partial | AVCL goals
Damage assessment |  |  | Requires models of interest
Notes: http://en.wikipedia.org/wiki/Brevity_code

## Slide 16: Goal-based Mission Example, with constraints
Phase 1: Search Area A
Phase 2:
Sample Environment in Area A
Phase 3: Search Area B
Phase 4: Rendezvous with
UUV-2 in Area C
Succeed
Fail
Fail
Fail
Succeed
Succeed
MEA Start
Sample Environment Phase Controller
Area Definition
Sampling Requirements
Operational and Ethical Constraints Checking
Queries
Responses: Succeed
or
Fail
or
Constraint Violation
Tactical Level
System State and Sensor Data
Controller Parameters
Sensor Settings, Responses
Phase 5: Transit
Return to Base
Succeed
Fail
Mission Abort
Mission Complete
Succeed
Fail
Execution Level
handles real-time control and response
Tactical-Level modules with shared vehicle state
and telemetry history
Vehicle
Commands
Strategic Level
Real-time orders
Tactics module sequencer
Surface
Recovery position
Constraint
Constraint
Constraint
Constraint
Constraint

## Slide 17: Constraints applied to sample mission
Constraint 1: The vehicle must maintain navigational accuracy within acceptable limits. * Applies to entire mission.
Constraint 2: All safety equipment must be fully functional. *
Constraint 3: All mission systems must be operational. Applies to Goal 1, Goal 2, and Goal 3.
Constraint 4: Acceptable distance from shipping lanes in the form of 1000 meter lateral standoff or minimum depth of 20 meters must be maintained. Applies to Goal 1, Goal 2, Goal 3, and Goal 4.
Constraint 5: Must be able to detect surface contacts within 5000 meters. *
Constraint 6: Detected surface contacts are to be avoided by a minimum of 1000 meters. Applies to Goal 1, Goal 2, Goal 3, and Goal 4.
Constraint 7: Minimum depth of 20 meters is to be maintained. Applies to Goal 5.

## Slide 18: Challenge: broad implementation
Can we
  Define mission goals readable by humans + robots
  Produce actionable tasking for different AUVs
  Produce software examples that can run properly in simulation and in robots
Can we also
  Define goal constraints ethically and measurably
Yes
Initial tests successful

## Slide 19: Autonomous Vehicle Command Language (AVCL)
AVCL is a command and control language for humans running autonomous unmanned vehicles
  Close correspondence to human naval terminology
  Common XML representations for mission scripts, agenda plans, and post-mission recorded telemetry
Operators can utilize a single archivable and validatable format for robot tasking, results
  directly convertible to and from a wide variety of different robot command languages
https://savage.nps.edu/Savage/AuvWorkbench/AVCL/AVCL.html

## Slide 20: Example mission, as pseudo-code XML
<?xml version="1.0" encoding="UTF-8"?>
<UUVMission>
<GoalSet>
<Goal area=”A” id=”goal1”>
<Search nextOnSucceed=”goal2” nextOnFail=”goal3”/>
</Goal>
<Goal area=”A” id=”goal2”>
<SampleEnvironment nextOnSucceed=”goal3” nextOnFail=”recover”/>
</Goal>
<Goal area=”B” id=”goal3”>
<Search nextOnSucceed=”goal4” nextOnFail=”goal4”/>
</Goal>
<Goal area=”C” id=”goal4”>
<Rendezvous nextOnSucceed=”recover” nextOnFail=”recover”/>
</Goal>
<Goal area=”recoveryPosition” id=”recover”>
<Transit nextOnSucceed=”missionComplete” nextOnFail=”missionAbort”/>
</Goal>
</GoalSet>
</UUVMission>
XML is readable by human or robot,
captures logic of canonical mission

## Slide 21: Corresponding example: MEAMission.xml using AVCL xml

## Slide 22: AVCL mission goals support
AVCL mission goals | Define | Test | Definition
Attack | partial |  | To conduct a type of offensive action characterized by employment of firepower and maneuver to close with and destroy an enemy.
Decontaminate | √ |  | To provide purification making an area safe by absorbing, destroying, neutralizing, making harmless, or removing chemical, biological, or nuclear contamination.
Demolish | √ |  | To destroy structures, facilities, or material by any available means.
IlluminateArea | √ |  | To provide locale lighting by searchlight or pyrotechnics.
Jam | √ |  | To deliberately radiate, re-radiate or reflect electromagnetic energy with the object of impairing the use of electronic devices or systems.
MarkTarget | √ |  | To make visible (by the use of light, infrared, laser, smoke, etc.) of an object in order to allow its identification by another object.
MonitorTransmissions | √ |  | To conduct electronic warfare support operations with a view to searching, locating, recording and analyzing radiated electromagnetic energy.
Patrol | √ | √ | To gather information or carry out a security mission.
Rendezvous | √ | partial | Achieve a meeting at a specified time and place.
Reposition | √ | √ | To change position from one location to another.
SampleEnvironment | partial |  | Collect environmental samples for testing for chemical compounds, biological creatures, or nuclear hazards.
Search | √ | √ | To look for lost or unlocated objects or persons.

## Slide 23: AUV Workbench
Autonomous Unmanned Vehicle Workbench supports underwater, surface and air vehicles
  physics-based mission rehearsal
  real-time task-level control of robot missions, and
  replay of recorded results
  Industry-friendly open-source license, Sourceforge
  Basis: RBM 3-level architecture, AVCL commands
Used to rehearse strategic-level MEAMission.xml
  https://savage.nps.edu/AuvWorkbench
Example
open-source
implementation

## Slide 24: 4 example missions, UUV and USV

## Slide 25: MeaMission.xml simulation preview
Search planning
produces waypoints
All searches complete
Launch
Recovery
Rendezvous not supported
All events logged
Notes: These results are similar to the previously shown user-driven example #3: rendezvous attempt fails, so robot returns for recovery

## Slide 26: MeaMission.xml simulation 0, launch

## Slide 27: MeaMission.xml simulation 1, transit

## Slide 28: MeaMission.xml simulation 2, search

## Slide 29: MeaMission.xml simulation 3, transit

## Slide 30: MeaMission.xml simulation 4, sample

## Slide 31: MeaMission.xml simulation 5, transit

## Slide 32: MeaMission.xml simulation 6, search

## Slide 33: MeaMission.xml simulation 7, rdvu fail

## Slide 34: MeaMission.xml simulation 8, transit

## Slide 35: MeaMission.xml simulation 9, recovery

## Slide 36: MeaMission.xml simulation 10, complete

## Slide 37: Mission definition observations
MEA formalism assumes human generation of mission orders
  Example expressed using AVCL
  Can also be expressed in other languages such as Java, Prolog, CLIPS rule sets, C++, etc.
  As shown in multiple RBM theses, dissertations
Key insight #3. Naval forces can only command mission orders that are:
  Understandable by (legally culpable) humans
  Reliably and safely executable by robots
Notes: This presentation demonstrates 2 implementations illustrating the example mission

## Slide 38: Humans + system validation that orders are well-defined together with ethically sound constraints

## Slide 39: Mission Execution Ontology (MEO)
Semantic Web supports well-defined expression of logical rules and relationships
Mission goals, capabilities, tasks and ethical requirements can be defined formally
  With tractable computation by reasoning engines
MEO applies Web Ontology Language (OWL), Resource Description Framework (RDF) lets mission correctness be validated logically
  Open standards, World Wide Web Consortium (W3C)
  Multiple proven implementations available

## Slide 40: Responsibility and accountability
Culpability, liability are problematic for AI agents
Command responsibility must be accompanied by Authority and Accountability
In this approach, humans remain responsible for correct mission tasking and approval of ethical constraints – preserving necessary oversight for release of potentially lethal force.
.

## Slide 41: Unmanned Vehicle Ethics Ontology
Mission
has_capability
Constraint
Goal
Vehicle
Goal_ Requirement
Vehicle_ Feature
can_identify
starts_with
includes
requires
can_fulfill
applies_to
applies_to
has_constraint
can_perform
has_feature
performable_by
Concepts
Roles
follows
End_ Condition
end_state
is_next
meets_requirement
Dashes indicate roles or concepts defined in terms of other roles or concepts
can_test
15 October 2014

## Slide 42: Example Mission Validation using Protégé Tool

## Slide 43: Review of take-away points
Humans in military units effectively deal with moral challenges without ethical quandaries.
Ethical behaviors don’t define mission plans; ethical constraints inform mission plans.
Naval personnel can only issue orders that are:
  Understandable by (legally culpable) humans, and
  Reliably and safely executable by robots.
Robot mission tasking can be carefully reviewed and approved by humans, with formal validation of correctness and ethical completeness.

## Slide 44: Influential student theses now possible
Define, explore core missions for today’s Navy
Use scenario simulations to test ethical challenges related to autonomous robot lethality
Apply ethical tasking to many unmanned systems, support military human-robot team concepts

## Slide 45: Contact
Don Brutzman, Ph.D.
brutzman@nps.navy.mil
brutzman@nps.navy.smil.mil
http://faculty.nps.edu/brutzman
Code USW/Br, Naval Postgraduate School
Monterey California 93943-5000 USA
1.831.656.2149 work
1.831.402.4809 cell

## Slide 46: Contact
Duane Davis, Ph.D.
dtdavi1@nps.edu
Code CS/Da
Naval Postgraduate School
Monterey California 93943-5000 USA
1.831.656.7980 work

## Slide 47: Contact
Curt Blais
clblais@nps.edu
Code MV/Bl
Naval Postgraduate School
Monterey California 93943-5000 USA
1.831.656.3215 work

## Slide 48: Contact
Robert B. McGhee, Ph.D.
robertbmcghee@gmail.com
Professor Emeritus
Computer Science
Naval Postgraduate School
Monterey California 93943-5000 USA

## Slide 49: ETHICAL MISSION TASKING AND EXECUTION FOR MARITIME ROBOTS
Lethality requires ethical & legal basis, supervised by military teams.
Effective robot tasking can resemble tactical tasking of humans afloat.
Careful application of goal constraints makes ethical control feasible.
Robot missions then complement and extend naval operation orders.
Semantic Web logic can confirm ethical correctness and completeness.
Next steps: extend 2 decades of work with simulation scenario testing.
Draft paper, IEEE/MTS OCEANS 2016 Conference, Monterey CA, 19-23 SEP 2016.
Authors Don Brutzman, Duane Davis, Curtis Blais, and Robert McGhee, NPS.
Review requests and feedback are welcome. Contact: brutzman@nps.edu
“Ethical constraints on robot mission execution are possible today. There is no need to wait for future developments in Artificial Intelligence (AI). It is a moral imperative that ethical constraints in some form be introduced immediately into the software of all robots that are capable of inflicting unintended or deliberate harm to humans or property.” - Robert McGhee, April 2016
Notes: https://zxing.appspot.com/generator
ETHICAL MISSION TASKING AND EXECUTION FOR MARITIME ROBOTS: A PRACTICAL APPROACH, draft paper for IEEE/MTS 2016.
All review comments welcome. Please send requests to brutzman@nps.edu